## Slide 1: AI Communication and Networking Lab
Unit 4: Deep Learning Techniques for Radar Sensing and Communications
教師：伍紹勳
助教：劉鎧睿

## Slide 2: Course Outlines
Lab 1: Introduction to FMCW radar and radar sensing
Lab 2: Variational auto-encoder (VAE) for FMCW signal demodulation
Lab 3: Long-short term memory (LSTM) for channel tracking
Lab 4: Convolutional neural network (CNN) for angle of arrival estimation
Lab 5: Final project on deep-learning enhanced radar sensing

## Slide 3: Frequency Modulated Continuous Wave (FMCW)

## Slide 4: FMCW Signal
Frequency at time t :
(chirp rate)
Instantaneous phase :
initial phase
Transmit signal in the first sweep :
(Assume the initial phase = 0)
Transmit signal in the sweep :
: time from the start of the sweep,

## Slide 5: FMCW Radar
Received signal :
Dechirp of FMCW Signal :
Transmit signal :
Received signal :
Dechirp
(Assume target is static, )
Quantize into and into , where is the sampling interval

## Slide 6: Quantize IF Signal
Quantize into and into , where is the sampling interval
Use fast Fourier transform to find the peak frequency content, , out of
From m, we have and then

## Slide 7: FMCW Signals under Doppler Frequency Shift
Received signal :
Dechirp of FMCW Signal :
Transmit signal :
Received signal :
Dechirp
Quantize the Doppler Frequency Shift into , where is the Chirp interval

## Slide 8: Range-Doppler Map
Quantize into and into , where is the sampling interval
Doppler velocity
Quantize the Doppler Frequency Shift into , where is the Chirp interval

## Slide 9: Variational auto-encoder (VAE) for FMCW signal demodulation
教師：伍紹勳
助教：劉鎧睿

## Slide 10: Use FMCW for Transmitting QPSK
Received signal :
Dechirp of FMCW Signal :
Transmit signal :
Received signal at the target :
Dechirp after the phase lock loop, the offset between the TX and RX chirps:   0
(Assume target is static, )
Symbol duration over multiple chirps

## Slide 11: Dechirped QPSK Signal Vectors
Define a symbol interval:
Let the remaining carrier frequency Hz
Symbol Energy
：random noise vector ~ N(0,1)
The quantized received noisy QPSK symbol vector can be expressed as：
Sampling frequency Hz

## Slide 12: QPSK Demodulation with Variational Auto Encoder
Parameters’ settings：
  Data size：500 for training, 100 for testing
  Learning rate：0.00001
  Epochs：500
  Input：noisy QPSK symbols ; Output：estimated codes
Sigmoid
512
256
128
128
256
512
1100
1100
4
Learning curve
The estimated codes for testing data are all correct
The following tensorflow function is used as the loss function in the implementation of VAE：
(The VAE network is composed of fully-connected layers)
The maximum probability index represents the estimated code

## Slide 13: Artificial Neural Networks (ANNs)
A single artificial neuron
  Inputs :
  Weights :
  Bias :
  Activation or transfer function to
    Predict the output :
Canonical form of a NN
  Inputs :
  Output :
  Weights and bias :
  Forward propagation

## Slide 14: Approximation with Neural Networks
For general regression case, any reasonable function can be approximated to any degree of precision by a three-layer network with
  Input layer:
  A hidden layer of sigmoid units: hk, if m is arbitrarily large
  One layer of linear output units :
A simple proof
  Consider a continuous function of y = f (, with x = )  [0, 1], W.L.O.G
  It suffices to approximate with a such that and for any x  [, ], and any k = 1,..., n.
  Hidden units, hk, are numbered from 0 to n with hk having a threshold (bias):
  For x  [, ], all hk are zeros except for h0 = h1 =,…, hk=1
  ) can be realized with a NN with one input x, n+1 hidden threshold gate units
  Let the weights wk for hk be wk = k f = - with 0 f =
  If , then + , Q.E.D

## Slide 15: Experiment Steps
Use matlab code “ QPSK_Generate ” to generate training and testing datasets
Upload the VAE sample code “QPSK_Demodulation_with_VAE.ipynb ” to your Google Colaboratory
Upload the datasets to your Google Drive and create folder according to the python sample code
Train the VAE and test its demodulation ability with your testing dataset

## Slide 16: AoA Estimation of FMCW Signals

## Slide 17: The System Model
There are only one object, and the angle of arrial is equal to one of
We use covariance matrix (real part and image part) as the input of the CNN network to predict where target is (from five points)
The ULA with m antennas
: Noisy data vector
: Testing signal
: Additive noise
: Array factor
(Array factor will be shown in the next page)

## Slide 18: The Array Factor
The ULA with m antennas
The array factor presents the phase differences of the corresponding antennas.
Usually, we have

## Slide 19: Quantization of Angles of Arrival (AoA)
Steering vector
N-point FFT with N  M
if

## Slide 20: AoA Estimation with FFT
Fourier Matrix

## Slide 21: AoA Estimation with MUSIC
s.v.d
With the assistance of the MUSIC algorithm, we can derive signal space and noise space
We can detect the angle from the spectrum of
In the next page, we will use the covariance matrix as the input of the CNN network to predict the direction of the object.

## Slide 22: AoA Estimation with CNN
The example of the CNN structure of predicting which point the target is
There are only one object, and the angle of is only equal to
The loss function of the final output is computed by “tf.nn.softmax_cross_entropy_with_logits”
Students can examine the accuracy of prediction with different SNRs.
The CNN structure in this page is just an example, and you can create your own CNN structure to predict where the target is.